## Slide 1
2 tests to serve French surface water quality data
OGC Hydrology DWG Water Quality (WQ) Data Seminar
17/03/2021

## Slide 2
Overview
Water quality use cases overview
Test 1 - Full Linked data test
Test 2 - SensorThings API (with linkedData registries)
Analysis
Analysis

## Slide 3
Analysis
Water quality use case overview
Water quality station
River
samples
Water quality sampling point
Sampling act
Sample
Analysis
Result…
Environmental conditions (related obs)
Analysis
Result…
Sub-sample
Analysis
Result…
120 million analysis results …
Chemical concentration - Complete model
Analysis

## Slide 4
Analysis
Water quality use case overview
Chemical concentration - Simplified (implemented) model
Analysis
Water quality station
River
sampledFeature
Water
Sample
Analysis
Result…
Analysis
Result…
Environmental conditions (related obs)
Observation
Observation result
Water Sample (SF_Specimen)
River (ultimate fOI)
Other fOIs on the side (ex : river pertains to river basin)
Environmental Monitoring Facility (EF)
EF associated information
relatedSamplingFeature
fOi
fOi
relatedObservation
relatedObservation
relatedObservation
relatedObservation

## Slide 5
Analysis
Water quality use case overview
Biodiversity Observation – overall rationale
Analysis
Taxon field observation (I counted a Eel)
Taxon score
Taxon indice (ex : river fish indice)
Taxon field observation (I counted 2 Salmo trutta fario)
Taxon score
Related obs
Related obs
Related obs
Related obs
A lot of related Observations !

## Slide 6
Test 1 - Full Linked data test (2018)
1°/ Features from national standard mapped to international standards
  River : HY_Feature
  Stations : SOSA/smod:ef
  Water quality observation
    SOSA / O&M
  And loaded in a triple store
Analysis

## Slide 7
Test 1 - Full Linked data test
2°/ Map/align taxonomies
  to international ones
    Units of measure : QUDT
    Chemical parameters ChemID+
  to sister organization ones
    in France : IFREMER (Marine Agency), MNHN for Taxa naming both provides the link to international reference dataset
    CSIRO
Analysis

## Slide 8
Analysis
Test 1 - Full Linked data test
2°/ Map/align taxonomies
  Chemistry
Geoscience ObjParSubs/3196
CHEBI/17632
ChemID+/14797-55-8
PubChem/943
CAS code
14797-55-8
« Nitrate »
Sandre PAR/1340

## Slide 9
Analysis
Test 1 - Full Linked data test
2°/ Map/align taxonomies
  Chemistry
Geoscience ObjParSubs/3196
CHEBI/17632
ChemID+/14797-55-8
PubChem/943
« Nitrate »
Sandre PAR/1340
http://purl.obolibrary.org/obo/CHEBI_17632
https://chem.nlm.nih.gov/chemidplus/rn/14797-55-8
https://pubchem.ncbi.nlm.nih.gov/compound/943
http://id.eaufrance.fr/par/1340
https://data.geoscience.fr/ncl/ObjParSubs/3196
owl:sameAs
owl:sameAs

## Slide 10
Test 1 - Full Linked data test
2°/ Map/align taxonomies
  Taxa naming
Sandre APT/2221
MNHN TAXREF-LD/67778
WoRMS/ 293723
« Salmo trutta fario »
Analysis

## Slide 11
Test 1 - Full Linked data test
2°/ Map/align taxonomies
  Taxa naming
Sandre APT/2221
MNHN TAXREF-LD/67778
WoRMS/ 293723
« Salmo trutta fario »
https://data.geoscience.fr/ncl/apt/2221
http://taxref.mnhn.fr/lod/name/67778
http://www.marinespecies.org/aphia.php?
p=taxdetails&id=293723
skos:exactMatch
skos:exactMatch
Analysis

## Slide 12
Test 1 - Full Linked data test
2°/ Map/align taxonomies
  Taxa naming
Sandre APT/2221
MNHN TAXREF-LD/67778
WoRMS/ 293723
« Salmo trutta fario »
IFREMER (French Marine Agency) / Quadrige² / 126281
GBIF
Catalogue of Life
Encyclopedia of Life
EUNOMEN PESI
ToBe refined
AlgeaBase
skos:exactMatch
skos:exactMatch
skos:exactMatch
Analysis

## Slide 13
Analysis
Test 1 - Full Linked data test
2°/ Map/align taxonomies experience
  Content exposed in a linked data registry
    https://data.geoscience.fr/ncl/
  Hard to have an external reference that
    Is community endorsed
    Have the same domain scope
    Provides resolvable URI and also semantic web artefacts (SPARQL endpoint, content negotiation,…)
  Sometimes one alignment provided a hook to many other repo in a given domain
    Ex : chemical parameters (ChemId+)

## Slide 14
Test 1 - Full Linked data test
3°/ demos - Chemical observation
Video https://github.com/INSIDE-information-systems/EnvironmentalSemanticWeb/blob/master/demos/chemical_observation.mp4
Analysis

## Slide 15
Test 1 - Full Linked data test
3°/ demos - Chemical observation

## Slide 16
Test 1 - Full Linked data test
3°/ demos - Chemical observation
Obs
Station
River
result
procedure
observedProperty

## Slide 17
Test 1 - Full Linked data test
3°/ demos - Hydrobiological observation (Taxa occurrence)
  Video https://github.com/INSIDE-information-systems/EnvironmentalSemanticWeb/blob/master/demos/bio_observation.mp4
Analysis

## Slide 18
Test 1 - Full Linked data test
3°/ demos - Hydrobiological observation (Taxa occurrence)
Station
Field Observation
Score (related Observation)
Indice(related Observation)
Field obsProp

## Slide 19
Test 2 – SensorThings API (2019)
New approach to lower the entry ticket
  API :
    OGC SensorThings API (OGC Sensor Observation Service ‘successor’)
    XML -> JSON
  Taxonomies : still in a linked Data Registry
  No Triple store for all observation, stations and river network elements
    Observations in ST API
    Minimal info for Rivers & Stations in ST API (for the rest, URI -> OGC WFS & OGC API – Feature description)
Only on chemical observations
No Taxa occurrence observation in this one
Analysis

## Slide 20
Analysis
Test 2 – SensorThings API
Chemical concentration - Simplified (implemented) model => mapped to ST API
Analysis
Water quality station
River
sampledFeature
Water
Sample
Analysis
Result…
Analysis
Result…
Environmental conditions (related obs)
Observation
Observation result
Water Sample (SF_Specimen)
River (ultimate fOI)
Other fOIs on the side (ex : river pertains to river basin)
Environmental Monitoring Facility (EF)
EF associated information
relatedSamplingFeature
fOi
fOi
relatedObservation
relatedObservation
relatedObservation
relatedObservation
Thing
fOI
Obs
Obs
SensorThings API classes

## Slide 21
Analysis
Test 2 – SensorThings API
Chemical concentration - Simplified (implemented) model => mapped to ST API
Monitoring
Facility
Water Sample
Observation on Sample
Observed property
Analysis procedure
om:parameter :
fraction, medium
River

## Slide 22
Analysis
Test 2 – SensorThings API
Introducing environmental conditions (ex : weather when sampling, …)
Water Sample
Environmental conditions when sampling

## Slide 23
Analysis
Test 2 – SensorThings API
Introducing environmental conditions (ex : weather when sampling, …)
Black three quality datastreams (at a
given station, obsProperty, procedure)
White : one environmental condition
datastream (at a given station, …)

## Slide 24
Test 2 – SensorThings API
3°/ Prototype demo
API4INSPIRE project
Data
French Biodiversity Office (OFB),
BRGM,
Land Baden-Württemberg (LUBV)
=> Several SensorThings API edpoints

## Slide 25
Test 2 – SensorThings API
3°/ Prototype demo

## Slide 26
Test 2 – SensorThings API
3°/ Prototype demo
  Focus on surface water quality stations

## Slide 27
Test 2 – SensorThings API
3°/ Prototype demo
OFB : LE RHIN À DRUSENHEIM
LUBV : bei Grauelsbaum (XX317.00)

## Slide 28
Test 2 – SensorThings API
3°/ Prototype demo
Vocabularies not mapped yet,
would be the ideal next step

## Slide 29
Test 2 – SensorThings API
3°/ Prototype demo
  Observations regarding Calcium

## Slide 30
Test 2 – SensorThings API
3°/ Prototype demo
  Observations regarding Calcium

## Slide 31
Conclusions
Corner stone for success is in vocabularies !
Pattern arising using Observations & Measurements
  From a domain point of view, water quality is more complex that automated river flow monitoring as it often involves (sub)sampling and a lot of related Observation
    In GWML2 we defined a ‘pattern’ on aquifer/pump tests eventhough everything is in O&M (https://docs.ogc.org/is/19-013/19-013.html#toc49 )
    We could achieve the same for WQ
  Evolutions in Observations & Measurements (& samples ! ) V3 will help
    Ex : on ultimateFOI / proximateFOI
Analysis

## Slide 32
Conclusions
Importance of sharing communities taxonomies
  Use of well-defined / shared controlled Vocab (codeLists) for Procedure, ObservedProperty etc…
  We have the same context & endeavor here as many other organizations
  How to we organize ourselves to trigger momentum ?
  Map to each other ? to a reference point ?
  At least let’s share some practices
This presentation is about SurfaceWater Quality
  All this is also valid for GroundWater Quality
Analysis

## Slide 33
Thank you & thanks to
s.grellet@brgm.fr
a.feliachi@brgm.fr
h.bressan@brgm.fr
Kathi@DataCove.eu
hylke.vanderschaaf@iosb.fraunhofer.de